R.E.S. INTEGRATION

RURAL SUSTAINABLE DEVELOPMENT THROUGH INTEGRATION OF RENEWABLE ENERGY TECHNOLOGIES IN POOR EUROPEAN REGIONS

Specific Targeted Research Project (FP6-509204)

##### WORK PACKAGE 2: Identify schemes for IRES implementation

| Project Acronym | R.E.S. INTEGRATION |
| --- | --- |
| Project Full Title | Rural sustainable development through integration of renewable energy technologies in poor European regions |
| Contract number | FP6-509204 |
| Type of action | Specific Targeted Research Project |
| Project duration | 1st November 2004 – 31st October 2007 |
| Project coordination | AUA – Agriculture University Of Athens, Greece |
| Contact persons Germany WIP | Maurice Pigaht M.Eng. WIP - Renewable Energies Tel: +49 89 72012724 Fax: +49 89 72012791 maurice.pigaht@wip-munich.de www.wip-munich.de |  |
| Document’s title | DELIVERABLE No 4: Sustainability pathways |
| Date | 30 September 2005 |

Project supported by the European Commission

within the 6th framework Programme

Specific measures in support of

International Co-operation - Western Balkan Countries (INCO-WBC)

http://www.cordis.lu/fp6/inco.htm

Sustainable Energy Pathways – Achental and Leukental

| Project title | Communal Biogas Plant at the Sewage Works |
| --- | --- |
| Short description of intervention | A pre-feasibility study has been done for a biogas plant that will produce several useful products for the community: 1. Electricity production sold to the national grid; 2. Waste disposal of green cuttings; 3. Compost production; 4. Heat production for the adjacent sewage works |
| Driving forces | The driving forces behind the project are financial (the plant is profitable and reduces the running costs of the sewage works) and a new law in Germany that obliges municipalities to dispose of their own green cuttings. |
| Supporting instruments | The German feed-in tariff of about 18.2c/kWh (dependant on size of plant and fuel source) |
| Identification of local actors | A newly founded communal company in which the shareholders are all the affected municipalities. The sewage works WIP allied with a local engineering company (Finsterwalder Umwelttechnik) |
| Description of the project | Pre-feasibility study due by 15/10/05 Plant could be operational by late 2006 |
| Energy objectives | Fuel: 2000t/a green cuttings 6000t/aliquid manure per annum 6000t/a energy crops (corn sillage) per annum Production: 509kW heat (80kW process heat for the sewage works, 300kW for sewage drying, 170kW for additional pruposes ) 327kW electricity sold to the grid |
| Environmental benefits | Improved energy economy. Reduced GHG emissions |
| Socio-economic benefits | Approx 1 job for a plant operator Approx 0.5 jobs for raw material/manure logistician |
| Environmental & sustainability issues | Visual and smell pollution resulting from the plant need to be kept hidden from nearby population centers. |
| Economics | Payback time of 3-4 years |

| Project title | Communal PV Plant |
| --- | --- |
| Short description of intervention | A PV plant is planned for the valley using public and private roof space for the installation of grid-connected PV systems. |
| Driving forces | Financial (feed-in tariff), and as a common successful RE project for the region. |
| Supporting instruments | Feed-in tariff of 57.4c/kWh |
| Identification of local actors | Newly founded company owned by the municipalities as a plant operator (Ökomodell Achental GmbH) WIP in cooperation with GreenCity e.V as project engineers Local investors: municipalities and private persons from the target region. |
| Description of the project | Pre-feasibility study in 2005 Project plan in 2006 Operation in 2006 |
| Energy objectives | 1.2MW of new PV installations |
| Environmental benefits | Reduced GHG emissions |
| Socio-economic benefits | Increased energy autonomy Additional rural income |
| Environmental & sustainability issues | Only visual issues (integration into the rural scenery/architecture very important) |
| Economics | Payback time in 10-15 years depending on insolation and site characteristics |

| Project title | Wessner Hof – Marquartstein Germany |
| --- | --- |
| Short description of intervention | biogas is produced in a fermenter biomass: disposal liquid manure from pigs and bulls, food left-overs from restaurants biogas is used in two bock heat and power plant An extension of the biogas plant is planned for 2006 |
| Driving forces | The produced biogas is used to heat the own hotel and the own house, produce hot water and to gain electrical energy. |
| Supporting instruments | Feed-in tarif of 18.2c/kWh for the new plant if correct fuels are used (currently the operator receiveds around 11c |
| Identification of local actors | Wessner Hof |
| Description of the project | 1996 the biogas plant was built with two heat and power plants unrestricted running time extension is planed in 2006 or 2007 |
| Energy objectives | for each bock heat and power plant: installed thermal power: 160kW installed electrical power: 80kW Extension planned to double thermal and electric power to 320kW and 160kW respectively |
| Energy Demand by sector to be covered in % | heat power is used by own consumption electrical power is feeded in the public grid |
| Environmental benefits | Improved energy autonomy. Useage of waste material Reduction of methane emmissions Reduction of CO2 emmissions |
| Socio-economic benefits | no new workplace amount of work: 1h/d increased to about 2h/d |
| Environmental & sustainability issues | There is a ranger of the smell reaching nearby population centres. |
| Economics | total costs: 100.000€ government subsidy: 45.000€ Cost of plant extension likely to be higher (around 150 000 Euro) with no government subsidy |